## Slide 1
Error and Correction Simulation of CEPC Booster and Damping Ring
Daheng Ji (IHEP)
on behalf of CEPC AP group
4. July. 2023, Edinburgh, The 2023 International Workshop on CEPC

## Slide 2: Content
CEPC Booster
  Booster design
  Error set
  Correction
CEPC positron damping ring
  Damping ring design
  Error Set
  Correction
Summary

## Slide 3: Booster optics
TME like structure (cell length=78m)
Interleave sextupole scheme
Emittance@120GeV=1.26nm
D. Wang, C. H. Yu, Y. M. Peng…
Arc cell
Overall idea: uniform distribution for the Q
Combined magnet (B+S) scheme possible
Phase advance/cell: 100 (H) / 28 (V)
Dispersion sup.
Half ring

## Slide 4
Error Set in Simulation
3σ cutoff | Dipole | Quadrupole | Sextupole
Transverse shift X/Y (μm) | 100 | 100 | 100
Longitudinal shift Z (μm) | 100 | 150 | 150
Tilt about X/Y (mrad) | 0.2 | 0.2 | 0.2
Tilt about Z (mrad) | 0.1 | 0.2 | 0.2
Nominal field | 1e-3 | 2e-4 | 3e-4
 | Accuracy (m) | Tilt (mrad) | Gain | Offset w/ BBA (mm)
BPM(10Hz) | 1e-7 | 10 | 5% | 30e-3
dipole | quadrupole
B1/B0  210-4 | 
B2/B0  510-4 | B2/B1  310-4
B3/B0  210-5 | B3/B1  210-4
B4/B0  810-5 | B4/B1  110-4
B5/B0  210-5 | B5/B1  110-4
B6/B0  810-5 | B6/B1  510-5
B7/B0  210-5 | B7/B1  510-5
B8/B0  810-5 | B8/B1  510-5
B9/B0  210-5 | B9/B1  510-5
B10/B0  810-5 | B10/B1  510-5
  #BPM~2400
  #Corrector~1200
Simulation based on Accelerator Toolbox(AT).

## Slide 5: Correction Process
Orbit Correction + Horizontal dispersion
Optics correction
Coupling and vertical dispersion correction

## Slide 6: Correction Process
Orbit Correction + Horizontal dispersion
  Response Matrix
  2-level iteration：
    1st Loop: 20%~100% Corrector
    2nd Loop：30%~80% Singular Value
  Dispersion correction
  Energy adjustment by corrector
  80um RMS in both plan
Optics correction
Coupling and vertical dispersion correction
@30GeV

## Slide 7: Correction Process
Orbit Correction + Horizontal dispersion
  Response Matrix
  2-level iteration：
    1st Loop: 20%~100% Corrector
    2nd Loop：30%~80% Singular Value
  Dispersion correction
  Energy adjustment by corrector
  80um RMS in both plan
Optics correction
  RM + LOCO
  Based on 30GeV simulation
  All quadrupole independent
  Dispersion correction included
Coupling and vertical dispersion correction
RMS@30GeV | X | Y
Orbit (mm) | 0.080 | 0.080
Beta Beating(%) | 0.8 | 0.38
Δ Dispersion(mm) | 2.7 | 3.5
@30GeV

## Slide 8: Correction Process
Orbit Correction + Horizontal dispersion
  Response Matrix
  2-level iteration：
    1st Loop: 20%~100% Corrector
    2nd Loop：30%~80% Singular Value
  Dispersion correction
  Energy adjustment by corrector
  80um RMS in both plan
Optics correction
  RM + LOCO
  Based on 30GeV simulation
  All quadrupole independent
  Dispersion correction included
Coupling and vertical dispersion correction
  Mainly used for the simulation of beam polarization. (Z. Duan)
  Skew quadrupole magnets are arranged in both the dispersion free section and the arc section to correct coupling and vertical dispersion independently.
  the coupling control target being better than 0.5%

## Slide 9
DA@30GeV
Tracking by SAD (1500 turns)
include errors (w. multipole errors)
Include SR sawtooth orbit (without taper)
Include SR damping & fluctuation
On axis injection from Linac to booster
BSC definition (inj=6.5nm):
Energy acceptance: 3*inj =0.45%
Dou Wang, Daheng Ji

## Slide 10
DA@45GeV
Tracking by SAD (1200 turns)
include errors (w. multipole errors)
Include SR sawtooth orbit (without taper)
Include SR damping & fluctuation
Off axis injection from booster to collider
BSC definition (x=0.18nm, y=x *1%):
Energy acceptance: 4* =0.15%
Dou Wang, Daheng Ji

## Slide 11
DA@80GeV
Tracking by SAD (500 turns)
include errors (w. multipole errors)
Include SR sawtooth orbit (without taper)
Include SR damping & fluctuation
Off axis injection from booster to collider
BSC definition (x=0.56nm, y=x *1%):
Energy acceptance: 4* =0.27%
Dou Wang, Daheng Ji

## Slide 12
DA@120GeV
Tracking by SAD (250 turns)
include errors (w. multipole errors)
Include SR sawtooth orbit (without taper)
Include SR damping & fluctuation
On axis injection from booster to collider
BSC definition (x=1.26nm, y=x *1%):
Energy acceptance: 5* =0.5%
Dou Wang, Daheng Ji

## Slide 13
DA@180GeV
Tracking by SAD (150 turns)
include errors (w. multipole errors)
Include SR sawtooth orbit (with taper)
Include SR damping & fluctuation
Keep possibility for on axis injection to collider
BSC definition (x=2.84nm, y=x *1%):
Energy acceptance: 4* =0.59%
--
--
Dou Wang, Daheng Ji
(On-axis)
(Off-axis)
Taper:
The DA deteriorated significantly when the beam energy exceeds 120GeV.
Taper the dipoles and quadrupoles can obviously improve the DA.
The approximate effect can be obtained by grouped dipoles which can significantly reduce the cost

## Slide 14: Content
CEPC Booster
  Booster design
  Error set
  Correction
CEPC positron damping ring
  Damping ring design
  Error Set
  Correction
Summary

## Slide 15
Phase/cell: 60/60
Interleave sextupole scheme
2 sex. families
DR optics
Arc
B=1.28T
Cell length: 3m
B=1.28T
r /0=0.355
-r
0
Parameters | Dipole | Quadrupole | Sextupole
Transverse shift X/Y (μm) | 100 | 100 | 100
Longitudinal shift Z (μm) | 100 | 150 | 100
Tilt about X/Y (mrad) | 0.2 | 0.2 | 0.2
Tilt about Z (mrad) | 0.1 | 0.2 | 0.1
Nominal field | 1×10-3 | 2×10-4 | 3×10-4
Parameters | BPM (10 Hz)
Accuracy (m) | 1×10-7
Tilt (mrad) | 10
Gain | 5%
Offset after beam based alignment (BBA) (mm) | 30×10-3
Dipole | Quadrupole | Sextupoles
B1  2 |  | 
B2  3 | B2  3 | 
B3  0.2 | B3  2 | B3  10
B4  0.8 | B4  1 | B4  3
B5  0.2 | B5  1 | B5  10
B6  0.8 | B6  0.5 | B6  3
B7  0.2 | B7  0.5 | B7  10
B8  0.8 | B8  0.5 | B8  3
B9  0.2 | B9  0.5 | B9  10
B10  0.8 | B10  0.5 | B10  3

## Slide 16
Orbit correction only
  # BPMs 40
  #Correctors 30+30
Error study for DR
Daheng Ji, Dou Wang
RMS@30GeV | X | Y
Orbit (mm) | 0.58 | 0.56
Beta Beating(%) | 1.1 | 2.0
Δ Dispersion(mm) | 6.4 | 2.4

## Slide 17
Orbit correction only
  # BPMs 40
  #Correctors 30+30
Error study for DR
Daheng Ji, Dou Wang
RMS@30GeV | X | Y
Orbit (mm) | 0.58 | 0.56
Beta Beating(%) | 1.1 | 2.0
Δ Dispersion(mm) | 6.4 | 2.4
BSCx,y=5σinj_x,y+5mm
Energy acceptance: 8.3inj=1.5%

## Slide 18: Further Plan in the EDR
Injection to storage: Filling the gap in the simulation of the entire process commissioning.
  First-turn, injection correction program, longitudinal parameter optimization program, etc.
Fast measurement and correction: The application and evaluation of these fast correction programs for the CEPC Booster will be based on the TBT BPM measurement and correction program.
Optimization of correction elements layout: Reducing costs while maintaining performance
Dynamic errors and drift: jitter/vibration/ground drift ↔ feedback
Abnormal situations: Identification and handling in commissioning process
Notes: gaps in our research regarding the process from beam injection to beam storage.

## Slide 19: Summary
The TME structure (TDR) has the following characteristics
  Use combined magnet to reduce magnet mounts
  Reduce beam emittance
  Error sensitivity is optimized
Error effect and correction simulation
  The error requirements for the hardware system are basically determined
  Error and correction simulation process is clear
  The simulation shows that the linear parameters and DA can meet the requirements
The next study will focus more on the actual commissioning requirements.

## Slide 20: Thanks for your attention!

## Slide 21: Back up

## Slide 22: DR parameters in TDR
 | DR V3.0
Energy (Gev) | 1.1
Circumference (m) | 147
Number of trains | 2 (4)
Number of bunches/trian | 2
Total current (mA) | 12.4 (24.8)
Bending radius (m) | 2.87
Dipole strength B0 (T) | 1.28
U0 (kev/turn) | 94.6
Damping time x/y/z (ms) | 11.4/11.4/5.7
Phase/cell (degree) | 60/60
Momentum compaction | 0.013
Storage time (ms) | 20 (40)
0 (%) | 0.056
0 (mm.mrad) | 94.4
injection z (mm) | 4.4
Extract z (mm) | 4.4
inj (mm.mrad) | 2500
ext x/y (mm.mrad) | 166(97)/75(3)
inj /ext (%) | 0.18 /0.056
Energy acceptance by RF(%) | 1.8
fRF (MHz) | 650
VRF (MV) | 2.5
Longitudinal tune | 0.0387
Damping with reversed bending magnet
4 (max. 8)-bunch storage, storage time:20 (40) ms
Emittance: 2500 166/75 (97/3) mm.mrad
Flexibility for extr. emittance

## Slide 23
Design Parameters of Booster
Injection |  | tt | H | W | Z | 
Beam energy | GeV | 30 |  |  |  | 
Bunch number |  | 35 | 268 | 1297 | 3978 | 5967
Bunch charge | nC | 1.1 | 0.78 | 0.81 | 0.87 | 0.9
Single bunch current | A | 3.4 | 2.3 | 2.4 | 2.65 | 2.69
Beam current | mA | 0.12 | 0.62 | 3.1 | 10.5 | 16.0
Energy spread | % | 0.025 |  |  |  | 
Synchrotron radiation loss/turn | MeV | 6.5 |  |  |  | 
Momentum compaction factor | 10-5 | 1.12 |  |  |  | 
Emittance | nm | 0.076 |  |  |  | 
Natural chromaticity | H/V | -372/-269 |  |  |  | 
RF voltage | MV | 761.0 | 346.0 | 300.0 |  | 
Betatron tune x/y |  | 321.23/117.18 |  |  |  | 
Longitudinal tune |  | 0.14 | 0.0943 | 0.0879 |  | 
RF energy acceptance | % | 5.7 | 3.8 | 3.6 |  | 
Damping time | s | 3.1 |  |  |  | 
Bunch length of linac beam | mm | 0.4 |  |  |  | 
Energy spread of linac beam | % | 0.15 |  |  |  | 
Emittance of linac beam | nm | 6.5 |  |  |  | 
Extraction |  | tt | H |  | W | Z | 
 |  | Off axis injection | Off axis injection | On axis injection | Off axis injection | Off axis injection | 
Beam energy | GeV | 180 | 120 |  | 80 | 45.5 | 
Bunch number |  | 35 | 268 | 261+7 | 1297 | 3978 | 5967
Maximum bunch charge | nC | 0.99 | 0.7 | 20.3 | 0.73 | 0.8 | 0.81
Maximum single bunch current | A | 3.0 | 2.1 | 61.2 | 2.2 | 2.4 | 2.42
Beam current | mA | 0.11 | 0.56 | 0.98 | 2.85 | 9.5 | 14.4
Bunches per pulse of Linac |  | 1 | 1 |  | 1 | 2 | 
Time for ramping up | s | 7.1 | 4.3 |  | 2.4 | 1.0 | 
Injection duration for top-up (Both beams) | s | 29.2 | 23.1 | 31.8 | 38.1 | 132.4 | 
Current decay in Collider |  | 3% |  |  |  |  | 
Energy spread | % | 0.15 | 0.099 |  | 0.066 | 0.037 | 
Synchrotron radiation loss/turn | GeV | 8.45 | 1.69 |  | 0.33 | 0.034 | 
Emittance | nm | 2.83 | 1.26 |  | 0.56 | 0.19 | 
Betatron tune x/y |  | 321.27/117.19 |  |  |  |  | 
RF voltage | GV | 9.7 | 2.17 |  | 0.87 | 0.46 | 
Longitudinal tune |  | 0.14 | 0.0943 |  | 0.0879 | 0.0879 | 
RF energy acceptance | % | 1.78 | 1.59 |  | 2.6 | 3.4 | 
Damping time | ms | 14.2 | 47.6 |  | 160.8 | 879 | 
Natural bunch length | mm | 1.8 | 1.85 |  | 1.3 | 0.75 | 
Full injection from empty ring | h | 0.1 | 0.14 | 0.16 | 0.27 | 1.8 | 0.8