## Slide 1
Progress in the design
Of CEPC Detector Beampipe
Ji Quan
July 5, 2023

## Slide 2
Content:
General introduction
Detailed structure
Simulation analysis
Summary and Next plan

## Slide 3
General introduction
d. Carbon fiber cylinder
c. Air channel
b. The central Be pipe
a. The extending Al pipe
Vertex
LumiCal
LumiCal
BPM
BPM
General drawing
Extending pipe
Both sides : Double
Top and Bottom : Single
Basic Structure:
1) Components : a, b, c, d and e
2) Detectors : BPM, LumiCal and Vertex
e. Combination flange
Updated design :
1) Added detector : BPM
2) Extending pipe : From Conical pipe to Gradient runway
Total length : 1400 mm

## Slide 4
Detailed Structure
Three detectors --- BPM and LumiCal
Installation position
BPM
1. A 2 or 4 electrode-BPM is installed in
each flange
LumiCal
1. Near the flanges, axial length is 120mm
BPM : 2 or 4 electrodes
LumiCal

## Slide 5
Detailed Structure
Three detectors --- BPM and LumiCal
Installation and maintenance --- BPM
Outer half-ring protection cylinder
Outer big flange
BPM Maintenance status
Outer big flange
half-ring protection cylinder
Two or Four
Electrodes

## Slide 6
Detailed Structure
Three detectors --- BPM and LumiCal
Installation and maintenance --- LumiCal
Outer half-ring protection cylinder
Inner half-ring protection cylinder
LimuCal Maintenance status

## Slide 7
Detailed Structure
Three detectors --- Vertex
Air-cooled channels and support structures
Air-cooled inlet
Air-cooled inlet
Air-cooled outlet
Air-cooled outlet
Cooled structure :
Three layer air cooled channel
Take away
The heat generated
by chips and electronics
Three double layers
Four inlets , four outlets
Design requirement
T ≤ 20 °C
△T < 10 °C or 7 °C
Vibration < 1μm (?)
The Vertex detector contains only barrel part which
consists of three double layers

## Slide 8
Detailed Structure
The Central Be pipe
Cooling structure :
Double-layer pipe
HOM heat
Coolant :
H2O or Paraffin
Take away
Total length : 350 mm, Gap : 0.35mm(Coolant)
Thickness of outer Be pipe: 0.15 mm
Thickness of inner Be pipe: 0.20 mm

## Slide 9
Detailed Structure
The extending Al pipe --- Gradient runway type
Installation space for LumiCal
Thickness of single layer beryllium sheet : 1.5 mm
The extending Al pipe
Double layer
construction
Double layer
construction
HOM heat
Take away
HOM heat
Take away
Coolant : H2O
Total length : 525 mm

## Slide 10
Simulation analysis
Thermal analysis --- Beampipe
Try to decrease the surface temperature further to meet the requirements of detectors
Outer surface temperature of the beampipe : ≤ 20 °C
The design principle is to keep
the outer surface temperature as low as possible

## Slide 11
Simulation analysis
Thermal analysis --- Beampipe
HOM heat : (Half length)
From : Liu Yudong
Calculation errors
safety factors
Thermal load for calculation (Half length)
Thermal load on the inner surface of the beam pipe :
600 X 2 = 1200 W

## Slide 12
Simulation analysis
Thermal analysis --- Beampipe
Inlet temperature: 16℃
Inlet velocity : 0.8 m/s
Laminar
Coolant : Paraffin or H2O
4 inlet, 4 outlet
Inlet temperature: 16℃
Inlet velocity : 1 m/s
Turbulent
Coolant : H2O
2 inlet, 2oulet
Inlet temperature: 16℃
Inlet velocity : 1 m/s
Turbulent
Coolant : H2O
2 inlet, 2 outlet
Results
Of the overall
Coolant : paraffin
Coolant : H2O
Overall temperature field distribution
Highest temperature position(Transition section)
T(Max) : 31.1℃
T(Max) : 26.7℃

## Slide 13
Simulation analysis
Thermal analysis --- Beampipe (Central Be pipe)
Results
Of the Central Be pipe
Coolant : paraffin
Coolant : H2O
Outer surface temperature
of the outer Be pipe
Outer surface temperature
of the outer Be pipe
Δt=2.4 ℃
ΔP=37.3 kPa
Δt=1.0 ℃
ΔP= 21kPa
Transition section

## Slide 14
Simulation analysis
Thermal analysis --- Beampipe
Results
Of the extending Al pipe
Top temperature
Bottom temperature
Temperature of Be sheet
Section temperature distribution(x=585mm)
Outer surface temperature
of the extending Al pipe

## Slide 15
Summary and Next plan
Summary
1. The preliminary mechanical design of the beam pipe has been finished
2. About three detectors
On the Beampipe, the space has been reserved for LumiCal
Mechanical design of BPM and Vertex have been finished, and the interface design
with the beam pipe has been determined
3. The preliminary study on thermal analysis of beam pipe has been performed, the temperature could
meet the requirements.
Next plan
1. The optimization of the air-cooling scheme would be conducted based on the overall simulation.
2. The impact due to vibration for the Vertex must be studied and simulated
3. The corrosion between the coolant and the Be pipe must be studied

## Slide 16
Thanks